## Slide 1: Brocade Data center IP Launch - VDX 6740 and 6740T Switches
Suzette Pereira-Beardsley
Nishant Shah

## Slide 2: Agenda
Launch Overview
VDX HW and SW Roadmap
VDX6740
VDX6740T
Licensing and SKU Strategy
Migration Plan (VDX6710/20/30  VDX6740 Family)
Resources

## Slide 3: Fall Launch
Product Overview
NOS 4.0 (Leo)
High Availability/ISSU (8770)
VRF-Lite
Logical Chassis
Management and Dynamic Services
VDX 6740 & 6740T /T (Castor/CastorT)
  1 RU 48 x 10 SFP GE + 4 x 40 QSFP+ Ports (Castor)
  1 RU 48 x 10 10BASET GE + 4 x 40 QSFP+ Ports (Castor-T)
NOS 4.1 (Capricorn)
Cloud ID
VxLAN
Openflow
NAS Auto prioritization
Brocade Network Advisor 12.1
Provides visibility and control of Brocade VCS innovation
Focus on managing unique platform capabilities
Reporting
NOS 4.0
NOS 4.1
Available
07/25/13
Available
08/09/13
Available
08/09/13
Available
01/31/14
Announce
09/18/13

## Slide 4
L2 Ethernet Features
VCS
AMPP
vLAG (MCT)
End-to-End FCoE
iSCSI DCB TLV
VDX 6710 (Carme) –
1GE RJ45 Server Access
VDX 6730 (F-Calisto) – Calisto with FC ports for bridging
Increase VCS Scale
L2 Feature & security enhancements
BNA Support
Connectivity from VCS to FC SAN
Managability – SNMPv3
VDX Product Family & S/W Roadmap
Dec
2010
VDX8770 – VDX Modular Chassis, 4 & 8 I/O Slot, 48x1GE, 48x10G, 12x40G
L3 (OSPF, VRRPe)
Increased VCS scalability
4K vlan support
NOS2.0
NOS2.1
Nov
2011
Oct
2012
Shipping
NOS3.0
Shipping
July
2013
VDX 6740 - 48 port 1/10G SFP+, 4 QSFP
VDX 6740T- 48 port 10GBaseT, 4 QSFP
HA/ISSU
Logical Chassis
128K MAC address
VRFs
PVLAN
Metro VCS
F port on VDX6730
NOS4.0
VDX 6720 (Callisto)
10GbE SFP+ TOR
Dec
2010
Shipping
FCS
AUG 9th
JAN
2014
PBR for Dynamic Services Insertion
VXLAN Gateway
VM Ware NVP Integration
ClouldID/GVLAN
Auto NAS
DHCP Based FW and Config Upload
NOS4.1

## Slide 5: VDX 6740

## Slide 6: Brocade VDX 6740 – Next Generation VDX TOR Switch
8 Flex Ports
(FC/FCoE/Ethernet)
Brocade VCS Fabric technology
AMPP, VM-Aware Network automation, Fabric Watch
Logical Chassis – Single Point of Management for a VCS Fabric
Simplicity and Automation
48 X1/10Gbe SFP+ Support and 4 X 40GbE QSFP+
Single ASIC , Non-blocking, wire-speed cut-through architecture,
850ns any port to port latency , 24MB Deep buffers with Dynamic Buffering
L2/L3 Switching (1.28 TBPS, 960 MPPS)
10GbE to 160GbE Brocade Trunk support
Direct-attached copper, active optical, SFP optical , QSFP optics , and 10GbE Breakout connectivity options
160K MAC, 32K ARP, 12K ACL, 2K VXLAN, 256 port profiles
Port/Trunk Groups – 0 to 15, 16 to 31, 32 to 47, 48 to 49 , 50 to 51
Leading Performance and Density
32 Flex port (FCoE , Ethernet and FC connectivity)
Full IP storage support with DCB capability
Cloud ID/Fine Grained Label /VXLAN/NVGRE capable
IPv6 – Hardware Ready
Advance Capabilities and Storage Connectivity
Note : All the numbers mentioned on this slide are Hardware supported. For latest scale numbers check release notes
48X10GbE SFP+
(FCOE/Ethernet)
8 Flex Ports
(FC/FCoE/Ethernet)
16Flex Ports
(FC/FCoE/Ethernet)
4X40GbE QSFP+
1 RU
Single ASIC
1.2 Tbps
960 MPPS
850ns latency any Port to Port
With 24 MB Deep Buffer
Up to 160GbE Brocade Trunk
Notes: 6
Key Points
Highlight of the VDX 6720 switches.

## Slide 7: VDX6740 Trunk Group
Trunk Group 1
Trunk Group 2
Trunk Group 3
Trunk Group 4
Trunk Group 3A
Trunk Group 4A
Note:
The ports marked in Yellow are FC capable (Flex Ports), but the FC feature is not supported on VDX 6740 in the Leo Release.
Ports in Trunk Group 3 and 3A cannot be trunked together in Leo Release
Ports in Trunk Group 4 and 4A cannot be trunked together in Leo Release

## Slide 8: Brocade VDX 6740 Switch
Dual hot-swappable, load-sharing power supplies
System cooling fans integrated into the power supplies
Two types of FRUs supported – Exhaust and Intake
Rear View
Integrated Cooling Fans
Redundant Power Supplies (FRUs)

## Slide 9: Brocade VDX 6740 – Hardware Architecture
VDX 6740 Block Diagram
Mgmt
Main
CPU
1
2
11
13
12
47
48
1x10GbE
1
1
2
Control Plane Traffic
FCoE/Ethernet /FC **
Data Switching
VDX 6740 Layout
QSFP
1
2
3
4
Console
USB
Management Plane - OOB
3
3
1x40GbE
ASIC
2
SFP+

## Slide 10: VDX 6740T

## Slide 11: Brocade VDX 6740T – Next Generation VDX TOR Switch
48X10Gbase-T (Ethernet/FCOE)
Brocade VCS Fabric technology
AMPP, VM-Aware Network automation.
Logical Chassis management support - Single IP management
Brocade Fabric Watch provides proactive monitoring and notification of critical switch component failure
Simplicity and Automation
48 X1/10Gbe SFP+ Support and 4 X 40GbE QSFP+
Single ASIC , Non-blocking, wire-speed cut-through architecture,
3us any port to port latency , 24MB Deep buffers with Dynamic Buffering
L2/L3 Switching (1.28 TBPS, 960 MPPS)
10GbE to 160GbE Brocade Trunk support
RJ45 copper, QSFP+ , QSFP+ to 4 SFP+ connectivity options
160K MAC, 32K ARP, 12K ACL, 2K VXLAN, 256 port profiles
Port/Trunk Groups – 0 to 15, 16 to 31, 32 to 47, 48 to 49 , 50 to 51
Leading Performance and Density
Cloud ID/ Fine Grained Label /VXLAN/NVGRE capable
IPv6 – Hardware Ready
Advance Capabilities
Note : All the numbers mentioned on this slide are Hardware supported. For latest scale numbers check release notes
Single ASIC
1.2 Tbps
960 MPPS
3us latency any Port to Port
With 24 MB Deep Buffer
Up to 160GbE Brocade Trunk
4X40GbE QSFP+
1 RU
Notes: 11
Key Points
Highlight of the VDX 6720 switches.

## Slide 12
Trunk Group 1
Trunk Group 2
Trunk Group 3
Trunk Group 4
Trunk Group 3A
Trunk Group 4A
Note:
The ports marked in Yellow are FC capable (Flex Ports), but the FC feature is not supported on VDX 6740 in the (NOS 4.0) Leo Release.
VDX6740T Trunk Group

## Slide 13: Brocade VDX 6740T Switch
Dual hot-swappable, load-sharing power supplies
5 Redundant cooling fans
Two types of FRUs supported – Exhaust and Intake
Rear View
Redundant Cooling Fans
Redundant Power Supplies (FRUs)

## Slide 14: Brocade VDX 6740T – Hardware Architecture
VDX 6740T Block Diagram
Mgmt
Main
CPU
1
2
8
12
47
48
1x10GbE
1
1
2
Control Plane Traffic
FCoE/Ethernet /FC **
Data Switching
VDX 6740T Layout
QSFP
1
2
3
4
Micro USB
Console
USB
48X10G Base T
RJ-45
1
Management Plane - OOB
3
3
1x40GbE
AQ-PHY
1
AQ-PHY
AQ-PHY
AQ-PHY
1 2
ASIC
2

## Slide 15: Licensing & SKU Strategy

## Slide 16: Licensing Strategy – VDX6740/VDX 6740T
NOTE : For VDX 8K L3 license is sold separately . VDX 6K includes L3 license in Base version.
Two node VCS , does not require any VCS license. More than 2 nodes in a VCS fabric would require VCS license on all nodes
1 – New in NOS 4.0
Layer3
(OSPF, VRRPe, PIM, BGP1, VRF-Lite1 )
FCOE License
$12,000
VCS License
(Logical Chassis Included1)
$7,000
ALLSW SKU(VCS+FCOE+L3)
$15,000
VDX 6740/ VDX 6740T(24P, 48P, 64P , 64P-ALLSW SKU)
24P
SKU
8 Port
DPOD
license
8 Port
DPOD
license
8 Port
DPOD
license
2X40Gb
DPOD
license
2X40Gb
DPOD
license
64P
48P
Breakout
Enabled for
40GbE ports

## Slide 17: VDX 6740 SKU Structure
VDX6740/VDX6740T HW SKU | Description
BR-VDX 6740-24 (-F/-R) | VDX 6740, 24P SFP+ PORTS ONLY- NO OPTICS, AC, NONPORT SIDE/PORT SIDE EXHAUST AIRFLOW
BR-VDX 6740T-24(-F/-R) | VDX 6740T, 24P 10GBase-T PORTS ONLY- NO OPTICS, AC, NONPORT SIDE/PORT SIDE EXHAUST AIRFLOW
BR-VDX6740-48(-F/-R) | VDX 6740, 48P SFP+ PORTS ONLY- NO OPTICS, AC, NONPORT SIDE/PORT SIDE EXHAUST AIRFLOW
BR-VDX6740T-48(-F/-R) | VDX 6740T, 48P 10GBase-T PORTS ONLY- NO OPTICS, AC, NONPORT SIDE/PORT SIDE EXHAUST AIRFLOW
BR-VDX6740-64(-F/-R) | VDX 6740, 64P SFP+ (Includes 48X10GB+ 4X40GB QSFP) PORTS ONLY- NO OPTICS, AC, NONPORT SIDE/PORT SIDE EXHAUST AIRFLOW
BR-VDX6740T-64(-F/-R) | VDX 6740T, 64P (Includes 48X 10GBase-T+ 4X40GB QSFP) PORTS ONLY- NO OPTICS, AC, NONPORT SIDE/PORT SIDE EXHAUST AIRFLOW
BR-VDX6740-64-ALLSW(-F/-R) | BR-VDX6740-64+VCS License + FCoE License
BR-VDX6740T-64-ALLSW(-F/-R) | BR-VDX6740T-64+VCS License + FCoE License
VDX6740/VDX6740T SW-SKU | Description
BR-VDX-6740-FCoE | FCoE License for 24P/48P/64P SKUs (VDX6740/VDX6740T)
BR-VDX6740-VCS | VCS License for 24P/48P/64P SKUs (VDX6740/VDX6740T)
BR-VDX6740-ALLSW | FCoE+ VCS License (VDX6740/VDX6740T)
BR-VDX6740-8X10G-POD | Port on demand license for 24P SKUs (VDX6740/VDX6740T)
BR-VDX6740-2x40G-POD | Port on demand 2X 40GB License for 24P/48P SKUs (VDX6740/VDX6740T)

## Slide 18: Supported OPTICS (NOS 4.0)
Optics | Description
E1MG-SX-OM (1-pack) E1MG-SX-OM-8 (8-pack) | 1000Base-SX
E1MG-LX-OM (1-pack) E1MG-LX-OM-8 (8-pack) | 1000Base-LX
10G-SFPP-SR (1-pack) | 10 Gbps SR
10G-SFPP-SR-8 (8-pack | 
10G-SFPP-LR (1-pack) | 10 Gbps LR
10G-SFPP-LR-8 (8-pack) | 
10G-SFPP-TWX-0101 (1-pack) | 1 m Twinax copper cable
10G-SFPP-TWX-0108 (8-pack) | 
10G-SFPP-TWX-0301 (1-pack) | 3 m Twinax copper cable
10G-SFPP-TWX-0308 (8-pack) | 
10G-SFPP-TWX-0501 (1-pack) | 5 m Twinax copper cable
10G-SFPP-TWX-0508 (8-pack) | 
40G-QSFP-SR4 | 40Gbps SR4
40G-QSFP-SR4-INT | 40Gbps SR4 (4X10 Gbps SFPP Break out capable)

## Slide 19: Brocade VDX 6740T Switch
Supported Cable Types

## Slide 20
Migration Strategy VDX6710/20/30 VDX6740 Family

## Slide 21: Fabric ISSU - Transient State
Transient Fabric State support during single maintenance window for smooth migration from NOS A to NOS B
NOS A
NOS A
NOS A
NOS B
NOS A
NOS A
NOS A
NOS B
NOS B
ISSU
ISSU
NOS B
NOS B
NOS B
Multi-Stage VDX Node Upgrade resulting in minimum fabric wide traffic disruption.
Around 500ms traffic convergence delay during fabric upgrade.
Recommended to have all nodes in a fabric to be upgraded to the same NOS software version.

## Slide 22: Adding VDX6740T to existing VCS fabric VDX6740T can only make a Fabric with VDX8770/VDX6740 in NOS4.0
Step 2 : Perform Fabric ISSU and Upgrade all the existing node to NOS4.X
NOS 4.X
NOS 4.X
NOS 4.X
NOS 4.X
NOS 4.X
NOS 4.X
NOS 4.X
NOS 4.X
NOS 4.X
NOS 4.X
NOS 4.X
Step 1 : Plan your Fabric ISSU under planned maintenance window
NOS A
NOS A
NOS A
NOS A
NOS A
VDX6710/20/30
VDX6710/20/30
VDX6710/20/30
VDX8770
VDX8770
VDX6710/20/30
VDX6710/20/30
VDX6710/20/30
VDX8770
VDX8770
Step 3 : Add VDX6740T to existing VCS fabric with VDX6710/20/30 and VDX8770
Note:
VDX6740T can ONLY form ISL with VDX8770/VDX6740 through 40GbE Ports. (ISL on Breakout are not supported in NOS 4.0)
VDX6740T can not form an ISL with VDX6710/20/30 at NOS4.0
ISL on 40Gbe Breakout will be supported in NOS 4.1 and VDX6740T will be able to form an ISL with VDX6710/20/30
NOS 4.X
ISL on 40G
VDX6710/20/30
VDX6710/20/30
VDX6710/20/30
VDX6740T
VDX8770
VDX8770
VDX6740T

## Slide 23: Adding VDX6740 to existing VCS fabric
NOS A
NOS A
NOS A
NOS A
NOS A
Step 2 : Perform Fabric ISSU and Upgrade all the existing node to NOS4.X
NOS 4.X
NOS 4.X
NOS 4.X
NOS 4.X
NOS 4.X
NOS 4.X
NOS 4.X
NOS 4.X
NOS 4.X
NOS 4.X
NOS 4.X
Step 1 : Plan your Fabric ISSU under planned maintenance window
VDX6710/20/30
VDX6710/20/30
VDX6710/20/30
VDX8770
VDX8770
VDX6710/20/30
VDX6710/20/30
VDX6710/20/30
VDX8770
VDX8770
Step 3 : Add VDX6740 to existing VCS fabric with VDX6710/20/30 and VDX8770
NOS 4.X
VDX6710/20/30
VDX6710/20/30
VDX6710/20/30
VDX6740
VDX8770
VDX8770
VDX6740
Note:
ISL on 10GbE SFP+ and 40GbE QSFP+ ports are supported. ISL on breakout are not supported in NOS 4.0
ISL on 40GbE Breakout will be supported in NOS 4.1.

## Slide 24: Resources

## Slide 25: New Collateral Resources – VDX 6740 & NOS 4.0
VDX 6740 Datasheet
VDX 6740 Product Overview Presentation
Updated 6710, -20, -30, 8770 datasheets
Logical Chassis Whitepaper
Updated TDM Presentation
BNA Product Overview Presentation
Updated BNA Datasheet, Ordering Guide, Features Brief
Collateral will be available on FlightDeck on 8/9

## Slide 26
THANK YOU

## Slide 27
BACKUP

## Slide 28: Leo Features
Feature Deployment Gaps
Feature Gaps | Workaround | Expected Resolution
Logical Chassis with HA (8770 MM Failover) | None, Recommend Active-Active at Spine | Capricorn
VRF Route Leak | Map the VRFs on FW to leak routes | Capricorn
VRF Scale (32 VRFs) | Propose Cloud-ID based designs | Taurus
SVI on PVLAN | SVI on a separate router (Shared Services Router) | Hardware Limitation
STP Scale | Propose Combination of STP and ELD (Targeting ~500 STP Ports, 250 ELD Instances) | Taurus
Breakout ISL on 40G/QSFP | None, Recommend 40G Spine | Capricorn
IPv6 Routing | Propose Vyatta Based Solutions | Taurus
IP Helper Functionality | ICX in One ARM Mode | Capricorn
Per VRF BGP | None, Propose OSPF for Per VRF IGP | Taurus

## Slide 29
NOS 4.0 (LEO)

## Slide 30: NOS 4.0 Release
Release Contents and Segment Alignment
Public Clouds
Managed Private Clouds
Managed Hosting
Enterprise Data Center
Flat
LAN
SAN
Target Segments
1Supported on VDX 87XX only
  Logical Chassis Management
  Single IP based NETCONF
Manageability
  VRF-Lite, BGP
  Private VLAN
Multitenancy
  Large Fabrics (32 Nodes)
  Port Profiles, MAC, ACL, ARP
Scalability
  In Service Software Upgrade1
  Hitless Failover1
Resiliency
  UDLD, RSPAN
  VCS Mode STP, ACL Based QoS
Evolutionary
Notes: Software outline. We have aligned out software strategy to our strategic segments:
Cloud Providers: Multitenancy, Scalability and Resiliency – required for building high scalable multitenant data center for their customers. In additional would require resiliency at Fabric level and node level. PVLAN is required for Cloud management network.
Managed Hosting Providers: They have similar needs as Cloud Providers with likely smaller scale and more versatility.
Enterprise DC and Private Cloud: Require Private VLANs for guest networks among other features.
All the segments require enhance manageability and automation which is a key deliverable on this release in terms of Logical Chassis Management. PBR based service insertion is a step towards services and eventually automating those services through programmatic control a al SDN.

## Slide 31: Leo (NOS 4.0) Features
Features, Functionality and Target Segments
New Functionality | Features | Segments
Resiliency | L2 ISSU, L2 HA, Management Module Failover | Enterprise DC Cloud Providers
Manageability | Logical Chassis Management | All
Multitenancy | VRF, Private VLANs | Cloud Providers
IP Routing | BGP, Per VRF OSPF | Cloud Providers
Layer-2 | VCS Mode STP, Foundry Interop Mode, | Enterprise DC, Hosting Providers
Other/Operational Enhancements | ACL Based QoS, ACL Based Sflow RSPAN, UDLD, vCenter LLDP, Range CLI | All, Relevant to Existing Customers
Scalability | 32 Node Fabric, 1000 Port Profiles, 128K MAC | Cloud Providers

## Slide 32: Logical Chassis Management
conf
conf
conf
conf
CLI
SNMP
Third Party Orchestration Tools
Virtual IP Management
conf
conf
Syslog
Logical Chassis Management
Single Point Virtual IP Management
Single Shared Config. File
Command redirection to the destination
R-bridge
Single point firmware download
Switch Replacement
conf
conf
conf
conf
conf
Virtual IP Owner
VCS Internal Mgmt Link

## Slide 33: Multi Layered-HA Infrastructure Battles DC Outages
Infrastructure built for resiliency
Unplanned Downtime
Planned Downtime
In-Service Software Upgrade
Fabric HA
System HA
Linecard HA
Data Center Outages
Layered Failover Architecture
User Unplanned Downtime to occur due to unforeseen incidents – VCS Layered Architecture provides HA in depth for non-disruptive recovery.
User Planned Downtime to occur due to Network Maintenance – In-Service Software Upgrades to provide network upgrade without impact on traffic
Multi Layered HA Infrastructure
Notes: Single, Unified software implementation across Brocade’s VDX
  Single CLI interface across platforms.

## Slide 34: Multi Layered HA Infrastructure Overview
VCS
Layered approach provides for a much resilient HA Architecture
Fabric HA
System HA
Line Card HA
Deterministic Multipathing
Reroutes traffic during failure without any convergence
Active – Active link Resiliency with vLAG support
Hitless Management Module Failover
In Service Software Upgrade
Virtualized Linecards for Active/Standby Images
Eliminate Linecard restarts during ISSU
VCS Multi Layered HA Architecture
New
NOS 4.0
Fabric
Differentiator
Unique
Differentiator
For full Multi- layered HA Overview, review presentation posted on Flight Deck

## Slide 35: NOS 4.0: Other Enhancements
Other Enhancements
Layer 3
  BGP
Security, Monitoring and Troubleshooting
  RSPAN
  UDLD
  ACL Based SPAN and Sflow and Rate Limiting
QoS
  ACL based QoS Assignment and Remarking
VCS Mode xSTP
  PVST+, RSTP, MSTP and STP – In VCS Mode
Distance Extension
  30 KM Long Distance ISL using WDM (Vendors: ADVA and Ciena)
  Encryption on Long Distance ISL using WDM (Vendors: ADVA and Ciena)
Direct Attached Storage (F-Port Connectivity on VDX 6730)

## Slide 36: Platform and Feature Compatibility for NOS 4.0
VDX 6710/6720/6730, VDX 6740, VDX 8770
Feature | 6720 ,6710, 6730 | 6740 | 8770
ISSU |  |  | 
Management Module Failover | NA | NA | 
VRF Lite |  |  | 
PVLANs |  |  | 
PIM in VCS Mode (Now 3.0.1) |  |  | 
STP in VCS Mode |  |  | 
RSPAN |  |  | 
ACL based QOS/Rate Limit/SFlow |  |  | 
Logical Chassis Management |  |  | 
Direct Attached Storage (F-Port) |  [VDX 6730 Only] |  | 
128K MAC |  |  | 
64K ARP |  |  | 
1024 Port Profiles |  |  | 
30KM Distance Extension using WDM |  [6730-76 and 6720-60 Only] |  | 